## Slide 1: Computer Architecture Spring 2020
Hamed Farbeh
farbeh@aut.ac.ir
Department of Computer Engineering
Amirkabir University of Technology
BASIC COMPUTER ORGANIZATION AND DESIGN

## Slide 2: Outlines
Computer Architecture-Spring 2020, AUT, Tehran, Iran
• Instruction Codes
• Computer Registers
• Computer Instructions
• Timing and Control
• Instruction Cycle
• Memory Reference Instructions
• Input-Output and Interrupt
• Complete Computer Description
• Design of Basic Computer
• Design of Accumulator Logic

## Slide 3: CONTROL UNIT
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Control unit (CU) of a processor translates from machine instructions to the control signals for the microoperations that implement them
Control units are implemented in one of two ways
Hardwired Control
  CU is made up of sequential and combinational circuits to generate the control signals
Microprogrammed Control
  A control memory on the processor contains microprograms that activate the necessary control signals
We will consider a hardwired implementation of the control unit for the Basic Computer

## Slide 4: TIMING AND CONTROL
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Control unit of Basic Computer
Instruction register (IR)
15
14 13 12
11 - 0
3 x 8
decoder
7 6 5 4 3 2 1 0
I
D
0
15 14 . . . . 2 1 0
4 x 16
decoder
4-bit
sequence
counter
(SC)
Increment (INR)
Clear (CLR)
Clock
Other inputs
Control
signals
D
T
T
7
15
0
Combinational
Control
logic

## Slide 5: TIMING SIGNALS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
- Generated by 4-bit sequence counter and 416 decoder
- The SC can be incremented or cleared.
- Example: T0, T1, T2, T3, T4, T0, T1, . . .
Assume: At time T4, SC is cleared to 0 if decoder output D3 is active.
D3T4: SC 0

## Slide 6: INSTRUCTION CYCLE
Computer Architecture-Spring 2020, AUT, Tehran, Iran
In Basic Computer, a machine instruction is executed in the following cycle:
  Fetch an instruction from memory
  Decode the instruction
  Read the effective address from memory if the instruction has an indirect address
  Execute the instruction
After an instruction is executed, the cycle starts again at step 1, for the next instruction
Note: Every different processor has its own (different) instruction cycle

## Slide 7: FETCH and DECODE
Computer Architecture-Spring 2020, AUT, Tehran, Iran
• Fetch and Decode
T0: AR PC (S0S1S2=010, T0=1)
T1: IR  M [AR], PC  PC + 1 (S0S1S2=111, T1=1)
T2: D0, . . . , D7  Decode IR(12-14), AR  IR(0-11), I  IR(15)
S2
S1
S0
Bus
7
Memory
unit
Address
Read
AR
LD
PC
INR
IR
LD
Clock
1
2
5
Common bus
T1
T0

## Slide 8: DETERMINE THE TYPE OF INSTRUCTION
Computer Architecture-Spring 2020, AUT, Tehran, Iran
= 0 (direct)
D'7IT3: AR M[AR]
D'7I'T3: Nothing
D7I'T3: Execute a register-reference instr.
D7IT3: Execute an input-output instr.
Start
SC  0
AR

PC
T0
IR

M[AR],
PC

PC + 1
T1
AR

IR(0-11),
I

IR(15)
Decode Opcode in IR(12-14),
T2
D7
= 0 (Memory-reference)
(Register or I/O) = 1
I
I
Execute
register-reference
instruction
SC

0
Execute
input-output
instruction
SC

0
M[AR]

AR
Nothing
= 0 (register)
(I/O) = 1
(indirect) = 1
T3
T3
T3
T3
Execute
memory-reference
instruction
SC

0
T4

## Slide 9: REGISTER REFERENCE INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
r = D7 IT3 => Register Reference Instruction
Bi = IR(i) , i=0,1,2,...,11
- D7 = 1, I = 0
- Register Ref. Instr. is specified in b0 ~ b11 of IR
- Execution starts with timing signal T3
Register Reference Instructions are identified when
r: SC  0
CLA rB11: AC  0
CLE rB10: E  0
CMA rB9: AC  AC’
CME rB8: E  E’
CIR rB7: AC  shr AC, AC(15)  E, E  AC(0)
CIL rB6: AC  shl AC, AC(0)  E, E  AC(15)
INC rB5: AC  AC + 1
SPA rB4: if (AC(15) = 0) then (PC  PC+1)
SNA rB3: if (AC(15) = 1) then (PC  PC+1)
SZA rB2: if (AC = 0) then (PC  PC+1)
SZE rB1: if (E = 0) then (PC  PC+1)
HLT rB0: S  0 (S is a start-stop flip-flop)

## Slide 10: MEMORY REFERENCE INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
AND to AC
D0T4: DR  M[AR] Read operand
D0T5: AC  AC  DR, SC  0 AND with AC
ADD to AC
D1T4: DR  M[AR] Read operand
D1T5: AC  AC + DR, E  Cout, SC  0 Add to AC and store carry in E
- The effective address of the instruction is in AR and was placed there during
timing signal T2 when I = 0, or during timing signal T3 when I = 1
- Memory cycle is assumed to be short enough to complete in a CPU cycle
- The execution of MR instruction starts with T4
Symbol
Operation
Decoder
Symbolic Description
AND D0 AC  AC  M[AR]
ADD D1 AC  AC + M[AR], E  Cout
LDA D2 AC  M[AR]
STA D3 M[AR]  AC
BUN D4 PC  AR
BSA D5 M[AR]  PC, PC  AR + 1
ISZ D6 M[AR]  M[AR] + 1, if M[AR] + 1 = 0 then PC  PC+1

## Slide 11: MEMORY REFERENCE INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Memory, PC after execution
21
0
BSA
135
Next instruction
Subroutine
20
PC = 21
AR = 135
136
1
BUN
135
Memory, PC, AR at time T4
0
BSA
135
Next instruction
Subroutine
20
21
135
PC = 136
1
BUN
135
LDA: Load to AC
D2T4: DR  M[AR]
D2T5: AC  DR, SC  0
STA: Store AC
D3T4: M[AR]  AC, SC  0
BUN: Branch Unconditionally
D4T4: PC  AR, SC  0
BSA: Branch and Save Return Address
M[AR]  PC, PC  AR + 1
Memory
Memory

## Slide 12: MEMORY REFERENCE INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
BSA:
D5T4: M[AR]  PC, AR  AR + 1
D5T5: PC  AR, SC  0
ISZ: Increment and Skip-if-Zero
D6T4: DR  M[AR]
D6T5: DR  DR + 1
D6T6: M[AR]  DR, if (DR = 0) then (PC  PC + 1), SC  0

## Slide 13: FLOWCHART for MEMORY REFERENCE INSTRUCTIONS
Computer Architecture-Spring 2020, AUT, Tehran, Iran
Memory-reference instruction
DR  M[AR]
DR  M[AR]
DR  M[AR]
M[AR]  AC
SC  0
AND
ADD
LDA
STA
AC  AC DR
SC  0
AC  AC + DR
E  Cout
SC  0
AC  DR
SC  0
D T
0
4
D T
1
4
D T
2
4
D T
3
4
D T
0
5
D T
1
5
D T
2
5
PC  AR
SC  0
M[AR]  PC
AR  AR + 1
DR  M[AR]
BUN
BSA
ISZ
D T
4
4
D T
5
4
D T
6
4
DR  DR + 1
D T
5
5
D T
6
5
PC  AR
SC  0
M[AR]  DR
If (DR = 0)
then (PC  PC + 1)
SC  0
D T
6
6


## Slide 14: to be continued
Computer Architecture-Spring 2020, AUT, Tehran, Iran